SEA LEVEL MONITORING IN SPAIN

National report for GLOSS

Begoña Pérez, Puertos del Estado, Spain

María Jesús García, Instituto Español de Oceanografía, Spain

At this moment there are 3 different institutions running the main tide gauge networks in Spain: Spanish Harbours (Puertos del Estado, PE), Spanish Institute of Oceanography (Instituto Español de Oceanografía, IEO) and the National Geographic Institute (IGN).

REDMAR: Spanish Harbours Tide Gauges Network: it is the more recent one, in operation since 1992. It was originally composed of 14 acoustic gauges (SRD) especially devoted to harbour applications and real-time use at the harbour. Nevertheless historical data have been continuosly processed and stored in a data base and data are provided freely for different research activities and with a symbolic price for commercial purposes. The network has been growing since year 2001 due to the demand of the ports authorities, and the actual number of stations is 23 (15 acoustic SRD gauges and 8 Aanderaa pressure sensors: details in http://www.puertos.es).

Along the years the need appeared of receiving  near real time sea level data not only by the personnel of the harbour but also by the responsibles of the network in Madrid, in order to provide a better maintenance and increase the service to the public. Since year 2000 data are transferred automatically via ftp or modem to Madrid, where an automatic quality control process is run before displaying data  on the web page and assimilating them in the storm surge forecasting system. For this last application data are required each 12 hours only, but data availability varies between 1 and 6 hours depending on the station.

Table 1: REDMAR network (Spanish Harbours)

| Site | Latitude | Longitude | Data available |
| --- | --- | --- | --- |
| Bilbao Santander Gijón A Coruña Villagarcía Vigo Huelva2 Sevilla (Bonanza) Sevilla (Esclusa)* Málaga Motril Valencia Barcelona Ibiza Tenerife Las Palmas Hierro Fuerteventura Granadilla Arinaga | 43º 20’ 14” N 43º 27’ 45” N 43º 33’ 33” N 43º 21’ 31” N 42º 35’ 58” N 42º 14’ 33” N 37º 08’ 00” N 36º 48’ 14” N 37º 19’ 57” N 36º 42’ 50” N 36º 43’ 23” N 39º 27’ 42” N 41º 21’ 01” N 38º 54’ 36” N 28º 28’ 42” N 28º 08’ 53” N 27º 48’ 00” N 28º 30’ 00” N 28º 05’ 00” N 27º 51’ 00” N | 03º 02’ 09” W 03º 47’ 22” W 05º 41’ 50” W 08º 23’ 17” W 08º 46’ 12” W 08º 43’ 35” W 06º 49’ 56” W 06º 20’ 10” W 05º 59’ 41” W 04º 24’ 52” W 03º 31’ 46” W 00º 19’ 33” W 02º 09’ 41” E 01º 26’ 36” E 16º 14’ 25” W 15º 24’ 27” W 17º 53’ 54” W 13º 51’ 06” W 16º 30’ 54” W 15º 24’ 00” W | 1992- 1992- 1996- 1992- 1997- 1992- 1996- 1992- 1992- 1992- 2004- 1992- 1992- 2003- 1992- 1992- 2003- 2003- 2003- 2003- |

* in Guadalquivir river, Sevilla harbour

Up to now, each of the REDMAR stations provides 5-minutes sea level data and, after a preliminary and automatic quality control, hourly values, harmonic constants, means and extremes are routinely obtained and published. Nevertheless, it is planned to decrease the time interval of raw data to 1 minute or less,  in order to use this information for detection of other local or external phenomena as seiches or tsunamis.

Figure 1: sea level stations belonging to the REDMAR Spanish Harbours Network

During the ESEAS-RI project a test station was established at Villagarcía de Arosa harbour (North West coast of Spain) in order to test different tide gauge techonlogies and especially to check the performance of  the new radar gauges. Details of this experiment can be found on the web page of ESEAS-RI project (http://www.eseas.org). It is possible that future REDMAR network will be based in some of the radar gauges tested there.

In June 2004 the first continuous GPS station of Spanish Harbours was installed collocated with the Ibiza tide gauge (Balearic Islands), also within the ESEAS-RI project.

Table1 shows coordinates and data availability of the different tide gauges of REDMAR.

The Spanish Institute of Oceanography Network:  established in 1943, most of the longer time series of sea level belong to this network of 12 stations based on float gauges. The complete equipment is composed of two different instruments: the classical mechanical float tide gauge (AOTT) and the data logger  (Allgomatic) . The mechanical float tide gauge is  constituted by a set of pulleys that transmit the movement of the float to a continuous graphical recorder.  The Allgomatic data logger is a system controlled by a microprocessor that registers, stores and transmits the data. It is connected to the float by a codifier that converts the lineal movement of the wire  float to a digital value, with millimeter precision. This system  has a telephone modem for data transmision from the station at the sea to the headquarter office. Sometimes the datalogger is a computer.

Table 2: Spanish Institute of Oceanography Network

| Site | Latitude | Longitude | Data available |  |
| --- | --- | --- | --- | --- |
| Santander A Coruña Vigo Cádiz Tarifa Ceuta Algeciras Málaga Palma de Mallorca Arrecife Puerto de la Luz Sta.Cruz de la Palma | 43º 27’ 45” N 43º 22’ N 42º 14’16” N 36º 32’ N 36º 00’ N 35º 54’ N 36º 07’ N 36º 42’ 50” N 39º 33’ N 28º 58’ 18” N 28º 08’ 53” N 28º 40’ 47” N | 03º 47’ 22” W 08º 24’ W 08º 43’ 51” W 06º 17’ W 05º 36’ W 05º 19’ W 05º 26’ W 04º 24’ 52” W 02º 38’ E 13º 31’ 48” W 15º 24’ 27” W 17º 45’ 59” W | 1943- 1943- 1943- 1949- 1943-1961,1963-1989,1991- 1943- 1943-1955,1961-2002 1943-1959, 1961- 1973-1982,1989-1993,1996- 1949-1975,1980- 1949-1956,1971-1989,1991- 1949-1989,1997- |  |

Table 2 shows the positions and availability of data of this network.

Figure 2: position of  IEO sea level stations

During two years an experiment has been carried out by this institution for testing the radar technology and as a result of this, plans have been made for renewing the equipment. This year two complete stations based on the radar will be purchased including sensor, datalogger or computer and real time data transmission. Most of the data from this institution can be downloaded from http://indamar.ieo.es/mareas/formulario_datos.htm.

A permanent  GPS station was also established by IEO during ESEAS-RI in Puerto de la Luz station (Canary Islands).

Data are retrieved weekly by phone, only occassionally this done daily. Plannings for this year include instalation of ADSL telephone line in several stations for real time data transmission.

The National Geographic Institute Network: this is the older one, with the first tide gauge installed in Alicante in XIX century and used as the reference for altitudes in Spain. The equipments are also classical float gauges with a data logger and modem connection (not automatic). The following table shows the stations and data availability, although exact coordinates of three of the stations are not available at the moment of doing this report. The other two are exactly at the same position than the corresponding REDMAR station.

Table 3: National Geographic Institute Network

| Site | Latitude | Longitude | Data available |  |
| --- | --- | --- | --- | --- |
| A Coruña Almería Alicante S.C Tenerife Fuerteventura | 28º 28’ 42” N 28º 30’ 00” N | 16º 14’ 25” W 13º 51’ 06” W | 1950-1980,1990- 1977-1999 1927-1939,1943-1946,1950- 1926-1936,1940-1991,1995- 1999-2002 |  |